## Slide 1: 次世代接取系統整合
Hung-Chi Chu
Department of Information and Communication Engineering
ChaoYang University of Technology

## Slide 2: Outline
次世代接取系統整合技術介紹
5QI規範介紹
多媒體通訊協定介紹
QoE Model分析介紹

## Slide 3: 1. 次世代接取系統整合技術介紹
The 3rd generation partnership project (3GPP) completed the first release of the fifth generation (5G) of mobile communications in its Release 15 in June 2018, which laid the basis for commercial 5G deployments worldwide. Since then, 3GPP has been working on the evolution of 5G technology in its Releases 16 and 17 to further improve performance and address new use cases. 3GPP recently approved the work package for its Release 18, which marks the start of 5G Advanced evolution. In this article, we provide an overview of the 5G Advanced evolution in 3GPP Release 18.

## Slide 5: Release 15
3GPP specified a new 5G air interface, known as New Radio (NR), aiming to address a variety of usage scenarios from enhanced mobile broadband (eMBB) to ultra-reliable low-latency communications (URLLC) to massive machine type communications (mMTC).
NR supports both non-standalone (NSA) operation, which utilizes Long Term Evolution (LTE) for initial access and mobility handling, and standalone (SA) operation without relying on LTE.
Key NR features include high-frequency operation and spectrum flexibility, ultra-lean design, forward compatibility, low-latency support, advanced antenna technologies, among others.

## Slide 6: Release 16
Introduces several major enhancements which not only improve existing features but also address new use cases and deployment scenarios.
Key improvements of existing features include multiple-input multiple-output (MIMO) and beamforming enhancements, enhanced support of dynamic spectrum sharing (DSS), reduced latency in dual connectivity (DC) and carrier aggregation (CA), and user equipment (UE) power saving.
The major new use cases and deployment scenarios addressed in Release 16 include enhanced support of industrial Internet of Things (IIoT) and URLLC, operation in unlicensed spectrum, vehicle-to-anything (V2X) communications, positioning services, and integrated access and backhaul (IAB).

## Slide 7: Release 17
Existing features, such as MIMO, DSS, UE power saving, coverage, positioning, and URLLC are further enhanced.
The major new use cases and deployment scenarios addressed in Release 17 include support for reduced capability (RedCap) UE, extension of NR operation to 71 GHz, multicast and broadcast service (MBS), and non-terrestrial networks (NTNs).
(Release 17 is the first time that 3GPP completes a full release of work all by electronic meetings.)

## Slide 8: Release 18
3GPP will continue to study and add functionality in Release 18 to enhance 5G performance by working in the areas of network energy savings, coverage, mobility support, MIMO evolution, MBS, and positioning.

## Slide 9: Network Energy Saving
Impetus for saving network energy has grown remarkedly as energy cost has become a major part of network operating expenses (OPEX). Besides, reductions in network energy consumption are imperative for operators to ultimately achieve the sustainability objective of net zero to help combat climate change.
5G NR is significantly more energy efficient in terms of energy consumption per bit than the previous generations of mobile technologies. However, due to increasingly dense deployment of 5G networks, use of massive MIMO, much larger bandwidths, and support of more frequency bands, 5G networks would lead to higher energy consumption if proper energy saving measures are not applied.

## Slide 10: Coverage Enhancement
Coverage is another key consideration for operators as it has a direct impact on service quality, capital expenditures (CAPEX), and OPEX in commercial deployments.
Uplink coverage is often found to be the bottleneck in commercial deployments. In Release 17, 3GPP has added techniques to extend uplink coverage for physical uplink shared channel (PUSCH) and physical uplink control channel (PUCCH). In Release 18, 3GPP plans to enhance the coverage of physical random access channel (PRACH), as well as studying techniques to increase UE power limit for CA and DC and reduce maximum power reduction (MPR) or peak-average-power ratio (PAPR). In addition, dynamic switching between cyclic-prefix (CP) orthogonal frequency-division multiplexing (OFDM) and discrete Fourier transform (DFT) spread OFDM (DFT-S-OFDM) in the uplink will be studied.

## Slide 11: Enhanced Mobility Support
Mobility support is a distinct feature of mobile networks which offers service continuity to moving UEs. When a UE moves from the coverage area of one cell to another, a handover process is initiated to change the serving cell for the UE. The change of serving cell is currently based on layer 3 (L3) measurements and radio resource control (RRC) signaling.
To reduce the latency, overhead, and interruption time associated with L3 based mobility management, mechanisms and procedures for layer 1 (L1)/layer 2 (L2) based inter-cell mobility will be introduced in 3GPP Release 18.
Another major area for Release-18 mobility work is to further enhance the support of conditional handover, in which UE receives a handover command with a condition from the network and does not apply the command until the condition is satisfied.

## Slide 12: MIMO Evolution
It has been observed in commercial deployments that UE with medium or high mobility experiences significant performance loss in multi-user MIMO (MU-MIMO) scenarios, partially due to outdated channel state information (CSI). Potential CSI reporting enhancements will be explored to improve performance for UE with medium or high mobility. Also, the work will study larger number of orthogonal demodulation reference signal (DMRS) ports for MU-MIMO. A unified transmission configuration indication (TCI) framework has been introduced in Release 17 for single transmission reception point (TRP).
3GPP will extend the TCI framework to multi-TRP scenarios and study coherent joint transmission, two timing advances (TAs), and enhanced uplink power control for multi-TRP. To better support advanced UEs such as customer premise equipment (CPE), fixed wireless access (FWA) devices, and vehicular UEs, support of eight antenna ports in uplink and simultaneous multi-panel uplink transmission will be investigated.

## Slide 13: Multicast and Broadcast
MBS is a feature dedicated to delivering multicast and broadcast services efficiently. Use case examples include television broadcasting, live video, software updates, and public safety usages.
3GPP specified the basic MBS support in Release 17, which enables multicast transmission to UEs in RRC connected state and broadcast transmission to UEs in all RRC states.
3GPP Release 18 will extend the multicast support to UEs in RRC inactive state, introduce enhancements to enable UEs in RRC connected state to simultaneously receive broadcast service and unicast service, and study mechanisms to improve resource efficiency in RAN sharing scenarios.

## Slide 14: Improved Positioning
Positioning is a valuable service that can find applications in diverse 5G use cases.
3GPP Release 18 will investigate solutions to further improve accuracy, integrity, and power efficiency in positioning, as well as studying sidelink positioning and positioning support for RedCap devices.

## Slide 15: Ranging based Services and Sidelink Positioning
Authorization and policy/parameter provisioning to UE.
Ranging/Sidelink Positioning device discovery
Operations for Ranging/Sidelink positioning
Network assisted Sidelink Positioning
Ranging service with the assistant UE
Ranging and sidelink positioning service exposure to a UE or Application server

## Slide 16: Flexible Spectrum Use
Spectrum is a scarce resource that needs to be used efficiently to achieve highest societal benefit. 3GPP Release 18 will introduce further enhancements to enable more flexible and efficient use of spectrum for 5G deployments in various scenarios with different spectrum allocations.

## Slide 17
The minimum channel bandwidth supported by the current 5G NR specifications is 5 MHz.
There are however growing interests in deploying NR in dedicated spectrum with less than 5 MHz bandwidth available for NR.
In Release 18, 3GPP will introduce necessary changes to NR to support deployments in spectrum allocations less than 5 MHz.

## Slide 18
DSS is a key 5G feature that enables a BS to use shared spectrum to provide connectivity to both LTE UE and NR UE. This facilitates the migration of spectrum from LTE to NR.
In DSS, the physical downlink control channel (PDCCH) capacity is a bottleneck, because NR PDCCH and LTE PDCCH need to share the first three OFDM symbols within a slot and NR PDCCH cannot use symbols overlapping with LTE cell-specific reference signal (CRS).
In Release 18, 3GPP will study the possibility of allowing NR PDCCH to be transmitted in symbols overlapping with LTE CRS to increase the PDCCH capacity for DSS. Also, the feature of configuring UE with multiple LTE CRS rate matching patterns in multi-TRP will be made available to single TRP scenario to help mitigate inter-cell interference.

## Slide 19
Time division duplex (TDD) is widely used in commercial 5G deployments. In TDD, downlink and uplink can use the entire frequency spectrum, but the time domain resource is divided between downlink and uplink.
NR supports TDD with semi-statically configured uplink/dowlink configuration, and dynamic TDD. If the time domain resource designated to uplink is limited, network performance such as coverage, capacity, and latency may be impacted.

## Slide 20
To enable more flexible spectrum use, 3GPP Release 18 will study the feasibility of allowing co-existence of downlink and uplink at the same time within a conventional TDD band.
  In other words, the duplex will become a mix of TDD and FDD.
From a practical standpoint, since full duplex is not mature enough for commercial deployments, the study will restrict its scope to sub-band non-overlapping full duplex at the 5G Node B (gNB) side. In other words, a conventional TDD band is divided into non-overlapping subbands and some are designated for uplink while others are designated for downlink, while half duplex is kept at the UE side.
3GPP Release 18 will study cross link interference (CLI) handling to better support dynamic TDD in commercial deployments.

## Slide 21: Diverse 5G Devices
5G needs to serve diverse types of devices across eMBB, URLLC, and mMTC usage scenarios. 3GPP Release 18 will continue to study and introduce tailored functionalities to enhance and expand 5G capabilities to serve not only smartphones but also other diverse 5G devices, such as extended reality (XR) and cloud gaming devices, low-complexity UEs, vehicular devices, and uncrewed aerial vehicles (UAVs).

## Slide 22: 5G Consumer Devices
A smartphone typically supports both 3GPP radio access technologies (RATs), e.g., LTE and NR, and non-3GPP RATs, e.g., WiFi. The coexistence of a 3GPP RAT and non-3GPP RATs may lead to interference and cause internal issue in the device.
In-device coexistence (IDC) is a feature that allows UE to indicate to its serving gNB that there is such coexistence issue in the UE. The gNB can utilize the indicated information to restrict radio resource usage to help resolve the UE's internal issue. The current IDC solution in NR has limited functionality.
3GPP Release 18 will enhance the feature by allowing UE to indicate the affected frequencies with finer granularity and its preferred TDD pattern.

## Slide 23
A multi-subscriber identity module (SIM) phone can be equipped with two independent SIM cards. When UE is only connected to one network (e.g., network A) using one SIM card, the UE's hardware resources can be dedicated to the communication with network A. Once the UE starts to connect to another network (e.g., network B) using the other SIM card, some of the hardware resources need to be used for communication with network B, but this is not known to network A.
3GPP Release 18 will enable the multi-SIM UE to indicate its preferred capability restriction to network A when the UE needs to communicate with network B.

## Slide 24
5G connected XR and cloud gaming devices are anticipated to proliferate in years to come.
In Release 17, 3GPP has conducted an evaluation study on XR to assess their performance when connected by 5G.
In Release 18, 3GPP will study enhancements to better support XR and cloud gaming devices in NR networks. The traffic generated in XR and cloud gaming use cases is often quasi-periodic and requires high data rate and bounded latency simultaneously. To efficiently serve such type of traffic, 3GPP will investigate resource allocation and scheduling mechanisms that can improve capacity for XR and cloud gaming devices. Since many XR and cloud gaming devices have limited battery power, Release 18 will also study UE power saving techniques to accommodate XR and cloud gaming service characteristics.
3GPP will investigate how to make RAN more XR-aware, including identifying what application information is beneficial for RAN to be aware of as well as how to utilize the information in RAN to handle XR and cloud gaming traffic.

## Slide 25: Support for eXtended Reality and Media Services (XRM)
Support for PDU set based QoS handling
  PDU set based QoS Parameters with PCF determination and provisioning, based on AF provisioned information
  PDU set information identification (e.g., PDU Set boundaries, PDU Set Importance, etc.) and marking by PSA UPF in GTP-U header over N3
5GS information exposure for XR/media enhancements
  Support for ECN marking for the purpose of L4S (Low Latency Low Loss Scalable throughput) by NG-RAN or by PSA UPF
  API based information exposure to AF e.g., radio congestion information
Other XRM related Enhancements
  Policy control enhancements to support multi-modality flows for single UE and multiple UEs, based on AF provisioned information.
  Uplink-downlink transmission coordination to meet round-trip latency requirements
  Policy enhancements for jitter minimization
  Enhancements to UE power savings for XR services
  Trade-off of QoE and power saving requirements

## Slide 27: 5G Devices for Verticals
While serving high-end eMBB devices are important in 5G NR networks, there have been growing interests in providing 5G connectivity to RedCap devices. Use cases include industrial sensors, video surveillance, and wearables, which require low UE complexity and low UE power consumption.
3GPP Release 17 has established a basic framework for supporting RedCap devices in NR networks. Built on the Release-17 foundation, 3GPP Release 18 will study enhancements to support RedCap devices of even lower complexity, targeting UE bandwidth reduction to 5 MHz and peak data rate reduction to 10 Mb/s in frequency range 1 (FR1).

## Slide 28
Devices such as industrial sensors and wearables have small form-factor and are power sensitive. UE power consumption depends on the configuration of discontinuous reception (DRX) cycle, e.g., paging cycle for UE in idle mode, because UE needs to wake up once per DRX cycle. When there is no signaling or data traffic, UE would wake up in vain and waste power. Therefore, it is beneficial to wake up UE when it is triggered.
Specifically, UE can be equipped with a separate receiver with ultra-low power consumption, which can monitor a wake-up signal. Upon detecting the wake-up signal, UE can trigger its main communication radio from off or deep sleep to become active.
3GPP Release 18 will study low-power wake-up receiver architectures and the design of wake-up signal, as well as procedure and protocol changes to support the wake-up receiver and signal.

## Slide 29
In many scenarios, low-power devices only need to support infrequent, small data transmissions. Transmitting such small data in RRC connected mode would lead to signaling overhead and delay.
To reduce signaling overhead and latency, 3GPP Release 17 introduced support for mobile originated small data transmission in RRC inactive mode.
In Release 18, 3GPP will introduce similar feature to support mobile terminated small data transmission in RRC inactive mode.

## Slide 30
3GPP continues to add functionality in Release 18 to enhance sidelink communication to support vehicular devices used in V2X services. One evolution objective is to increase sidelink data rate by adding CA feature in sidelink communication, extending sidelink operation to unlicensed spectrum, and enhancing sidelink support in frequency range 2 (FR2).
3GPP will study mechanisms to support LTE V2X and NR V2X devices co-existing in the same frequency channel.

## Slide 31
3GPP Release 18 will introduce 5G NR support for devices onboard aerial vehicles, i.e., UAVs, whose applications are proliferating across many industries. 3GPP has introduced 4G LTE support for UAVs back in Release 15, including enhanced measurement reports, reporting of UAV height, location and speed, flight path reporting, and signaling support for subscription-based aerial UE identification. These features will be introduced to 5G NR as appropriate. Besides, the work will study enhancements for broadcasting UAV identification and signaling to indicate UAV beamforming capabilities.

## Slide 32: Vehicle-Mounted Relays
Mobile base station relay (MBSR) configuration.
Efficient mobility and service continuity
  Moving UE
  Moving MBSR
Roaming of mobile base station relays
Location services for UEs accessing via a mobile base station relay
Control of UE's access to 5GS via a mobile base station relay

## Slide 33: Evolved Network Topology
Coverage is crucial for operators to provide competitive mobile services to their customers. Deploying full-stack BSs in coverage holes is a common way to improving network coverage, but it may not be always possible due to, e.g., lack of backhaul, economically not viable, among others. This calls for flexible network topology by increasing the resiliency of the split next-generation RAN (NG-RAN) architecture, exploiting diverse nodes such as IAB nodes, radio frequency (RF) repeaters, relays, and integration with NTNs.

## Slide 35
NG-RAN – the RAN for 5G – supports splitting a gNB into two parts: a centralized unit (CU) and one or more distributed units (DUs).
The gNB-CU can be further split into two parts: a control plane (CP) part and one or more user plane (UP) parts.
The logical gNB-CU-CP hosts the RRC and the CP part of the packet data convergence protocol (PDCP) of the gNB-CU.
Failures at the gNB-CU-CP may cause disruption to its connected gNB-CU-UPs and gNB-DUs, which in turn can impact the served UEs.
To enhance the resiliency of gNB-CU-CP, 3GPP Release 18 will study and identify gNB-CU-CP failure scenarios.

## Slide 36
IAB is a wireless backhaul solution based on NR. It serves as an alternative to fiber backhaul and thus can facilitate the deployment of mobile networks.
An IAB node may consist of two parts: mobile termination (MT) and DU.
The MT connects the IAB node to its donor node while the DU part can serve UEs and connect to other IAB nodes to create multi-hop wireless backhauling.
3GPP Release 18 continues to enhance NR-based IAB with a focus on the scenario where mobile IAB nodes are mounted on vehicles and provide 5G connectivity to UEs. To support mobile IAB nodes, the work will specify topology adaptation procedures, mobility enhancements for IAB nodes and the associated UEs, and interference mitigation.

## Slide 37
3GPP Release 18 will also enhance NR data collection within the scope of self-organizing network (SON)/minimization of drive testing (MDT). SON automates RAN planning, configuration, management, optimization, and healing, thereby minimizing human intervention.
3GPP Release 18 will study NR network-controlled repeater, which not only can amplify and forward the received signals but also can receive side control information from the gNB.
The side control information examples include beamforming information, TDD configuration, power control information, among others.
The study will identify which side control information is necessary, investigate needed L1/L2 signaling, and look into how to identify and authorize such network-controlled repeaters.

## Slide 38
Network coverage can also be extended by using a UE as a sidelink relay. The sidelink relay can be either a UE-to-network relay, where the relay UE connects a remote UE to the network, or a UE-to-UE relay, where the relay UE connects a first remote UE to a second remote UE.
In Release 17, 3GPP specified basic functionality support for UE-to-network relay.
3GPP Release 18 will enhance the support of UE-to-network relay, add support for UE-to-UE relay, and study multi-path support where a UE is connected to a gNB using one direct path and one indirect path via a sidelink relay.

## Slide 39
NTNs utilize satellites or high-altitude platforms (e.g., airplanes, balloons, and airships) to offer connectivity services. They can complement terrestrial networks by providing coverage in remote areas where terrestrial coverage is not available.
In Release 17, 3GPP has introduced a first set of basic features to enable NR operation over NTNs in FR1.
3GPP Release 18 will enhance NR operation over NTNs by improving coverage for handheld terminals, studying deployment in above 10 GHz, investigating regulatory requirement for network-verified UE location, and addressing mobility and service continuity between a terrestrial network and an NTN as well as between different NTNs.

## Slide 40: Satellite-related enhancements
5GC/EPC enhancements for satellite access (Phase 2)
  Mobility management and power saving enhancements in presence of discontinuous coverage
  Relies on provisioning satellite coverage maps:
    to the UE from an external server, and/or
    to the AMF via OAM or via AF
  Reuses existing Power Saving Mode (PSM) and Mobile Initiated Connection Only (MICO) features, considering the coverage maps
Support for 5G System with Satellite Backhaul
  Support of PCC/QoS control enhancement considering dynamic satellite backhaul and satellite backhaul information exposure
  Support of satellite Edge Computing via UPF on-board (applies to GEO satellite backhaul only)
  Support of local data switching via UPF on-board (applies to GEO satellite backhaul only)

## Slide 42: Enhanced support of Non-Public Networks
Support for enhanced mobility by enabling support for idle and connected mode mobility between SNPNs (standalone private networks) without new network selection
  Porting the concept of Equivalent PLMNs to SNPNs
Support for non-3GPP access to SNPN services
  Access to SNPN services using SNPN or Credentials Holder (CH) credentials for Untrusted non-3GPP access, Trusted non-3GPP access, Wireline access, Non-5G Capable WLAN (N5CW) devices
  Non-Seamless WLAN Offload (NSWO) for UEs using SNPN or CH credentials
Support for providing access to Localized Services

## Slide 43: Support for Deterministic Networking
Support for Deterministic Networking (DetNet), as standardized in the IETF
  Reuses the Time Sensitive Communications (TSC) framework for deterministic QoS and time synchronization services defined in Rel-17
  5GS acts as logical DetNet node/router
  Adds support for 5GS DetNet node reporting to the DetNet controller
  Adds support for provisioning of DetNet configuration from the DetNet controller to 5GS

## Slide 45: Support for Service Function Chaining (SFC) in 5GS
Traffic Steering Policy and SFC Enhancements
  Support for SFC in 5GS applies to non-roaming and Home-Routed roaming scenarios where the Application Function (AF) has an agreement with the HPLMN.
  An AF may request steering of user-plane traffic to a pre-configured chain of service functions on N6-LAN.
Exposure to enable AF to request predefined SFC for traffic flow(s) related with target UE(s)
  A Service Function Chain is identified by the SFC ID which is included in the AF request sent to the 5GC.
  The AF request may optionally include the Metadata information that is transparently passed to the UPF and provided by the UPF to the N6-LAN.

## Slide 47: Personal IoT Network (PIN)
Personal IoT Network (PIN) provides local connectivity between PIN elements i.e., UEs and/or non-3GPP devices.
A UE in a PIN Element with Gateway Capability (PEGC) can register with 5G network and act as 5G gateway for PIN elements to access 5G network.
PIN and PIN elements are managed by specific PIN element with Management Capability (PEMC) and the support from an Application Function (AF), if AF is deployed.
The AF for PIN may communicate with PEMC and PEGC via application layer for management of the PIN.
PEGC will map the PIN or PIN packets to an existing PDU session or establish a new PDU session based on the QoS markings.

## Slide 48
PIN: Personal IoT Network
PEGC: PIN Element with Gateway Capability
PEMC: PIN Element with Management Capability
PINE: PIN Element

## Slide 49: Data-Driven and AI-Powered 5G
5G networks are becoming increasingly complex while generating humongous data. It is crucial to be data-driven and leverage artificial intelligence (AI) techniques to efficiently manage the 5G networks. 3GPP Release 18 will not only enhance existing data collection features but also examine how AI techniques can improve air interface functions.

## Slide 50
In Release 17, 3GPP conducted a study on AI-enabled NG-RAN. The study investigated high-level principles, functional framework, potential use cases and their associated solutions for AI-enabled RAN intelligence. The identified AI solutions for the use cases require the collection of new information data as input to AI model training and AI model inference.
3GPP Release 18 will specify data collection enhancements and signaling support for a set of selective AI-based use cases including network energy saving, load balancing, and mobility optimization.

## Slide 51
3GPP Release 18 will also enhance NR data collection within the scope of self-organizing network (SON)/minimization of drive testing (MDT). SON automates RAN planning, configuration, management, optimization, and healing, thereby minimizing human intervention.
The measurement data collected from the RAN and UEs is the basis for the automatic decision making in SON. Drive tests measure network performance (e.g., coverage, interference, and capacity) or UE performance (e.g., call drop, throughput, and mobility performance).
MDT enables operators to configure normal UEs to collect and report measurement data to minimize traditional drive tests.
The Release-18 work will address SON features left over from Release 17, as well as data collection for random access channel (RACH) optimization.

## Slide 52
Besides data collection of radio related measurement and information, 5G NR quality of experience (QoE) management framework enables collection of measurement data at the application layer. The collected measurement data is used to assess user's satisfaction level of a service provided by mobile networks.
A QoE report contains data of QoE metrics collected at the application layer. Examples of QoE metrics in multimedia telephony service for internet protocol multimedia subsystem (IMS) include frame rate, jitter duration, round-trip time, average codec bit rate, among others.
In Release 17, 3GPP specified basic mechanisms for NR QoE management.
3GPP Release 18 will enhance the NR QoE framework to support new types of 5G services, such as XR, cloud gaming, and MBS.

## Slide 53
3GPP Release 18 will study AI/machine learning (ML) for NR air interface to enhance performance or reduce complexity/overhead. The study will establish a common AI/ML framework, identify areas where AI/ML can improve air interface functions, investigate how to describe and characterize AI/ML models, evaluate AI/ML techniques to understand their gains and complexity, and assess standardization impact.
To achieve these objectives, 3GPP will focus on a set of selective use cases including CSI feedback, beam management, and positioning. The study is expected to pave the way for other use cases leveraging AI/ML techniques in air interface.

## Slide 54: 5G system support for AI/ML-based Services
Support of network resource utilization monitoring for AI/ML application operations
  AF uses NWDAF based data analytics for Application AI/ML operation.
5GC Information Exposure to authorized 3rd party for Application Layer AI/ML Operation
Enhancing External Parameter Provisioning
5GC Enhancements to enable Application AI/ML Traffic Transport
QoS and Policy enhancements
  Existing QoS monitoring mechanisms for URLLC services are re- used.
  SMF send the info to UPF to binds the AI/ML traffic to distinctQoS flow.
5GS Assistance to Federated Learning Operation
  New member selection functionality was added that can providena list of recommended UEs based on the parameters contained in the request from the AF.

## Slide 55
UE triggers split inference. UE and an AI/ML server negotiate over application layer for the split inference operations.
The AF subscribes to one or more NWDAF analytics to generate the AI/ML Assistance information. AI/ML Assistance information from 5GC is needed to assist the AI/ML server to make corresponding decisions for the split inference.
Based on the assistance information and the current system environmental factors such as communications data rate, resource at UE, the AI/ML server AF makes decisions on split inference.

## Slide 56: 5QI
5QI stands for 5G QoS Identifier and it is equivalent to QCI in LTE. It just has more options and granularities. In addition, there is a new type called Delay Critical GBR which is not in QCI in LTE.

## Slide 57
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget | Packet Error Rate | Default Maximum Data Burst Volume (NOTE 2) | Default Averaging Window | Example Services
1 | GBR (NOTE 1) | 20 | 100 ms (NOTE 11, NOTE 12) | 10-2 | N/A | 2000 ms | Conversational Voice
2 |  | 40 | 150 ms (NOTE 11, NOTE 13) | 10-3 | N/A | 2000 ms | Conversational Video (Live Streaming)
3 |  | 30 | 50 ms (NOTE 11, NOTE 13) | 10-3 | N/A | 2000 ms | Real Time Gaming, V2X messages (see TS 23.287). Electricity distribution medium voltage, Process automation monitoring
4 |  | 50 | 300 ms (NOTE 11, NOTE 13) | 10-6 | N/A | 2000 ms | Non-Conversational Video (Buffered Streaming)
65 (NOTE 9, NOTE 12) |  | 7 | 75 ms (NOTE 7, NOTE 8) | 10-2 | N/A | 2000 ms | Mission Critical user plane Push To Talk voice (e.g., MCPTT)
66 (NOTE 12) |  | 20 | 100 ms (NOTE 10, NOTE 13) | 10-2 | N/A | 2000 ms | Non-Mission-Critical user plane Push To Talk voice
67 (NOTE 12) |  | 15 | 100 ms (NOTE 10, NOTE 13) | 10-3 | N/A | 2000 ms | Mission Critical Video user plane
75 (NOTE 14) |  | N/A | N/A | N/A | N/A | N/A | N/A
71 |  | 56 | 150 ms (NOTE 11, NOTE 13, NOTE 15) | 10-6 | N/A | 2000 ms | "Live" Uplink Streaming (e.g. TS 26.238)
72 |  | 56 | 300 ms (NOTE 11, NOTE 13, NOTE 15) | 10-4 | N/A | 2000 ms | "Live" Uplink Streaming (e.g. TS 26.238)
73 |  | 56 | 300 ms (NOTE 11, NOTE 13, NOTE 15) | 10-8 | N/A | 2000 ms | "Live" Uplink Streaming (e.g. TS 26.238)
74 |  | 56 | 500 ms (NOTE 11, NOTE 15) | 10-8 | N/A | 2000 ms | "Live" Uplink Streaming (e.g. TS 26.238)
76 |  | 56 | 500 ms (NOTE 11, NOTE 13, NOTE 15) | 10-4 | N/A | 2000 ms | "Live" Uplink Streaming (e.g. TS 26.238)

## Slide 58
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget | Packet Error Rate | Default Maximum Data Burst Volume (NOTE 2) | Default Averaging Window | Example Services
5 | non-GBR (NOTE 1) | 10 | 100 ms (NOTE 10, NOTE 13) | 10-6 | N/A | N/A | IMS Signalling
6 (NOTE 1) |  | 60 | 300 ms (NOTE 10, NOTE 13) | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g., www, e-mail, chat, ftp, p2p file sharing, progressive video, etc.)
7 |  | 70 | 100 ms (NOTE 10, NOTE 13) | 10-3 | N/A | N/A | Voice, Video (Live Streaming) Interactive Gaming
8 |  | 80 | 300 ms (NOTE 13) | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g., www, e-mail, chat, ftp, p2p file sharing, progressive video, etc.)
9 |  | 90 | 300 ms (NOTE 13) | 10-6 | N/A | N/A | Video (Buffered Streaming) TCP-based (e.g., www, e-mail, chat, ftp, p2p file sharing, progressive video, etc.)
69 (NOTE 9, NOTE 12) |  | 5 | 60 ms (NOTE 7, NOTE 8) | 10-6 | N/A | N/A | Mission Critical delay sensitive signalling (e.g., MC-PTT signalling)
70 (NOTE 12) |  | 55 | 200 ms (NOTE 7, NOTE 10) | 10-6 | N/A | N/A | Mission Critical Data (e.g. example services are the same as 5QI 6/8/9)
79 |  | 65 | 50 ms (NOTE 10, NOTE 13) | 10-2 | N/A | N/A | V2X messages (see TS 23.287)
80 |  | 68 | 10 ms (NOTE 5, NOTE 10) | 10-6 | N/A | N/A | Low Latency eMBB applications Augmented Reality

## Slide 59
5QI Value | Resource Type | Default Priority Level | Packet Delay Budget | Packet Error Rate | Default Maximum Data Burst Volume (NOTE 2) | Default Averaging Window | Example Services
82 | Delay critical GBR | 19 | 10 ms (NOTE 4) | 10-4 | 255 bytes | 2000 ms | Discrete Automation (see TS 22.261)
83 |  | 22 | 10 ms (NOTE 4) | 10-4 | 1354 bytes (NOTE 3) | 2000 ms | Discrete Automation (see TS 22.261); V2X messages (UE - RSU Platooning, Advanced Driving: Cooperative Lane Change with low LoA. See TS 22.185)
84 |  | 24 | 30 ms (NOTE 6) | 10-5 | 1354 bytes (NOTE 3) | 2000 ms | Intelligent transport systems (see TS 22.261)
85 |  | 21 | 5 ms (NOTE 5) | 10-5 | 255 bytes | 2000 ms | Electricity Distribution-high voltage (see TS 22.261); V2X messages (Remote Driving. See TS 22.186, NOTE 18, see TS 22.261)
86 |  | 18 | 5 ms (NOTE 5) | 10-4 | 1354 bytes | 2000 ms | V2X messages (Advanced Driving: Collision Avoidance, Platooning with high LoA. See TS 22.186, TS 23.287)
87 |  | 25 | 5 ms (NOTE 4) | 10-3 | 500 bytes | 2000 ms | Interactive Service - Motion tracking data, (see TS 22.261)
88 |  | 25 | 10 ms (NOTE 4) | 10-3 | 1125 bytes | 2000 ms | Interactive Service - Motion tracking data, (see TS 22.261)
89 |  | 25 | 15 ms (NOTE 4) | 10-4 | 17000 bytes | 2000 ms | Visual content for cloud/edge/split rendering (see TS 22.261)
90 |  | 25 | 20 ms (NOTE 4) | 10-4 | 63000 bytes | 2000 ms | Visual content for cloud/edge/split rendering (see TS 22.261)

## Slide 60
NOTE 1: A packet which is delayed more than PDB is not counted as lost, thus not included in the PER.
NOTE 2: It is required that default MDBV is supported by a PLMN supporting the related 5QIs.
NOTE 3: The Maximum Transfer Unit (MTU) size considerations in clause 9.3 and Annex C of TS 23.060 [56] are also applicable. IP fragmentation may have impacts to CN PDB, and details are provided in clause 5.6.10.
NOTE 4: A static value for the CN PDB of 1 ms for the delay between a UPF terminating N6 and a 5G-AN should be subtracted from a given PDB to derive the packet delay budget that applies to the radio interface. When a dynamic CN PDB is used, see clause 5.7.3.4.
NOTE 5: A static value for the CN PDB of 2 ms for the delay between a UPF terminating N6 and a 5G-AN should be subtracted from a given PDB to derive the packet delay budget that applies to the radio interface. When a dynamic CN PDB is used, see clause 5.7.3.4

## Slide 61
NOTE 6: A static value for the CN PDB of 5 ms for the delay between a UPF terminating N6 and a 5G-AN should be subtracted from a given PDB to derive the packet delay budget that applies to the radio interface. When a dynamic CN PDB is used, see clause 5.7.3.4.
NOTE 7: For Mission Critical services, it may be assumed that the UPF terminating N6 is located "close" to the 5G_AN (roughly 10 ms) and is not normally used in a long distance, home routed roaming situation. Hence a static value for the CN PDB of 10 ms for the delay between a UPF terminating N6 and a 5G_AN should be subtracted from this PDB to derive the packet delay budget that applies to the radio interface.
NOTE 8: In both RRC Idle and RRC Connected mode, the PDB requirement for these 5QIs can be relaxed (but not to a value greater than 320 ms) for the first packet(s) in a downlink data or signalling burst in order to permit reasonable battery saving (DRX) techniques.
NOTE 9: It is expected that 5QI-65 and 5QI-69 are used together to provide Mission Critical Push to Talk service (e.g. 5QI-5 is not used for signalling). It is expected that the amount of traffic per UE will be similar or less compared to the IMS signalling.

## Slide 62
NOTE 10: In both RRC Idle and RRC Connected mode, the PDB requirement for these 5QIs can be relaxed for the first packet(s) in a downlink data or signalling burst in order to permit battery saving (DRX) techniques.
NOTE 11: In RRC Idle mode, the PDB requirement for these 5QIs can be relaxed for the first packet(s) in a downlink data or signalling burst in order to permit battery saving (DRX) techniques.
NOTE 12: This 5QI value can only be assigned upon request from the network side. The UE and any application running on the UE is not allowed to request this 5QI value.
NOTE 13: A static value for the CN PDB of 20 ms for the delay between a UPF terminating N6 and a 5G-AN should be subtracted from a given PDB to derive the packet delay budget that applies to the radio interface.
NOTE 14: This 5QI is not supported in this Release of the specification as it is only used for transmission of V2X messages over MBMS bearers as defined in TS 23.285 [72] but the value is reserved for future use.

## Slide 63
NOTE 15: For "live" uplink streaming (see TS 26.238 [76]), guidelines for PDB values of the different 5QIs correspond to the latency configurations defined in TR 26.939 [77]. In order to support higher latency reliable streaming services (above 500ms PDB), if different PDB and PER combinations are needed these configurations will have to use non-standardised 5QIs.
NOTE 16: These services are expected to need much larger MDBV values to be signalled to the RAN. Support for such larger MDBV values with low latency and high reliability is likely to require a suitable RAN configuration, for which, the simulation scenarios in TR 38.824 [112] may contain some guidance.
NOTE 17: The worst case one way propagation delay for GEO satellite is expected to be ~270ms, ,~ 21 ms for LEO at 1200km, and 13 ms for LEO at 600km. The UL scheduling delay that needs to be added is also typically two way propagation delay e.g. ~540ms for GEO, ~42ms for LEO at 1200km, and ~26 ms for LEO at 600km. Based on that, the 5G-AN Packet delay budget is not applicable for 5QIs that require 5G-AN PDB lower than the sum of these values when the specific types of satellite access are used. 5QI-10 can accommodate the worst case PDB for GEO satellite type.

## Slide 64: Multimedia Protocol
Research on audio and video over packet-switched networks dates back to the early 1970s. The Internet Engineering Task Force (IETF) published RFC 741 in 1977 and began developing RTP in 1992, and would go on to develop Session Announcement Protocol (SAP), the Session Description Protocol (SDP), and the Session Initiation Protocol (SIP).
Real-time Transport Protocol (RTP) is designed for end-to-end, real-time transfer of streaming media. The protocol provides facilities for jitter compensation and detection of packet loss and out-of-order delivery, which are common, especially during UDP transmissions on an IP network.
RTP allows data transfer to multiple destinations through IP multicast. RTP is regarded as the primary standard for audio/video transport in IP networks and is used with an associated profile and payload format.

## Slide 65
Real-time multimedia streaming applications require timely delivery of information and often can tolerate some packet loss to achieve this goal. For example, loss of a packet in an audio application may result in loss of a fraction of a second of audio data, which can be made unnoticeable with suitable error concealment algorithms.
The Transmission Control Protocol (TCP), although standardized for RTP use, is not normally used in RTP applications because TCP favors reliability over timeliness. Instead, the majority of the RTP implementations are built on the User Datagram Protocol (UDP).

## Slide 66
RTP was developed by the Audio/Video Transport working group of the IETF standards organization. RTP is used in conjunction with other protocols such as H.323 and RTSP. The RTP specification describes two protocols: RTP and RTCP. RTP is used for the transfer of multimedia data, and the RTCP is used to periodically send control information and QoS parameters.
The data transfer protocol, RTP, carries real-time data. Information provided by this protocol includes timestamps (for synchronization), sequence numbers (for packet loss and reordering detection) and the payload format which indicates the encoded format of the data. The control protocol, RTP Control Protocol (RTCP), is used for quality of service (QoS) feedback and synchronization between the media streams. The bandwidth of RTCP traffic compared to RTP is small.

## Slide 67
RTP sessions are typically initiated between communicating peers using a signaling protocol, such as H.323, the Session Initiation Protocol (SIP), RTSP, or Jingle (XMPP). These protocols may use the Session Description Protocol to specify the parameters for the sessions.
An RTP session is established for each multimedia stream. Audio and video streams may use separate RTP sessions, enabling a receiver to selectively receive components of a particular stream.[14] The RTP and RTCP design is independent of the transport protocol. Applications most typically use UDP with port numbers in the unprivileged range (1024 to 65535).[15] The Stream Control Transmission Protocol (SCTP) and the Datagram Congestion Control Protocol (DCCP) may be used when a reliable transport protocol is desired. The RTP specification recommends even port numbers for RTP and the use of the next odd port number for the associated RTCP session.[16]: 68 A single port can be used for RTP and RTCP in applications that multiplex the protocols.
RTP is used by real-time multimedia applications such as voice over IP, audio over IP, WebRTC and Internet Protocol television.

## Slide 68
Internet
IP Layer
UDP Layer
Multimedia Content
TCP Layer
RTP Layer
RTCP Layer
RTSP/SIP Layer

## Slide 69: Real Time Transport Protocol (RTP)
A protocol is designed to handle real-time traffic (like audio and video) of the Internet, is known as Real Time Transport Protocol (RTP). RTP must be used with UDP. It does not have any delivery mechanism like multicasting or port numbers. RTP supports different formats of files like MPEG and MJPEG. It is very sensitive to packet delays and less sensitive to packet loss.
Applications of RTP :
  RTP mainly helps in media mixing, sequencing and time-stamping.
  Voice over Internet Protocol (VoIP)
  Video Teleconferencing over Internet.
  Internet Audio and video streaming.

## Slide 70: RTP Header Format

## Slide 71
Version : This 2-bit field defines version number. The current version is 2.
  P – The length of this field is 1-bit. If value is 1, then it denotes presence of padding at end of packet and if value is 0, then there is no padding.
  X – The length of this field is also 1-bit. If value of this field is set to 1, then its indicates an extra extension header between data and basic header and if value is 0 then, there is no extra extension.
  Contributor count – This 4-bit field indicates number of contributors. Here maximum possible number of contributor is 15 as a 4-bit field can allows number from 0 to 15.
  M – The length of this field is 1-bit and it is used as end marker by application to indicate end of its data.
  Payload types – This field is of length 7-bit to indicate type of payload. We list applications of some common types of payload.
  Sequence Number – The length of this field is 16 bits. It is used to give serial numbers to RTP packets. It helps in sequencing. The sequence number for first packet is given a random number and then every next packet’s sequence number is incremented by 1. This field mainly helps in checking lost packets and order mismatch.
  Time Stamp – The length of this field is 32-bit. It is used to find relationship between times of different RTP packets. The timestamp for first packet is given randomly and then time stamp for next packets given by sum of previous timestamp and time taken to produce first byte of current packet. The value of 1 clock tick is varying from application to application.
  Synchronization Source Identifier – This is a 32-bit field used to identify and define the source. The value for this source identifier is a random number that is chosen by source itself. This mainly helps in solving conflict arises when two sources started with the same sequencing number.
  Contributor Identifier – This is also a 32-bit field used for source identification where there is more than one source present in session. The mixer source use Synchronization source identifier and other remaining sources (maximum 15) use Contributor identifier.

## Slide 72: H.323
H.323 is one of the oldest standards which are generally used for VoIP telephony and video conferencing. It is a system of various protocols and elements that allows transferring media data over packet networks. This standard recommendation structure opens up different multimedia communication options, including telephony, video conferencing and media transfer.
One of the main benefits of H.323 standard is interoperability. With this internet protocol, solutions produced by different vendors can connect and operate with each other seamlessly.

## Slide 73
Endpoint is a tool used to manage H.323 device (sort of user interface). Endpoints can connect with each other using VoIP telephony or video conferencing mode.
Gateways are used to connect endpoints from various networks, e.g. H.323 and ISDN. By the way the gateway performs the following functions:
Establishing connection between endpoints;
Perform audio streams transcoding;
Signalling data exchange.
If the endpoints are in the same H.323 network, the gateways are not used.

## Slide 74
Zone controller or gatekeeper — is the central point of the H.323 network. It is responsible for addressing calls, manages bandwidth and defines authenticity of endpoints and gateways during connection. Although H.323 recommendation does not set gatekeeper as a required element, it is impossible to use many modern features implemented in VoIP applications and video conferencing solutions without gatekeeper.
Multipoint Control Unit (MCU) server is used to connect three or more endpoints during single session. All the endpoints participating in video conferencing are first connected to the MCU server, and then MCU distributes video streams to all the endpoints. MCU performs video streams transcoding in order to mix and downscale other participants video in a unique layout for every participants. This process require a lot of computational elements and resources which makes MCU a very expensive device. MCU device usually combines MCU, gateway and gatekeeper roles.

## Slide 75
H.323 Protocol Stack

## Slide 76
TCP:
  H.225. Establishing connection between H.323-devices.
  H.245. Exchanging information about new features (e.g. codecs supported). One endpoint "informs" the second endpoint about the capabilities supported (codecs) and selects a codec based on the capabilities of the second terminal.
UDP:
  RAS. Used between endpoints, gateways and gatekeeper. It is responsible for registration, calls and statuses resolution.
  RTP. Used for real-time media transmission through networks.
To terminate connection, the endpoints send a message to the gatekeeper. After that, the channel closes and the connection is terminated.

## Slide 77: H.323 Codecs
Audio exchange function is considered the main function of H.323 standards (as they had originally been used in VoIP telephony). Thus, each endpoint should support at least one codec from the G.7XX family.

## Slide 78
Video communications were positioned as secondary in respect to this standard. As a consequence, video codec support was not obligatory. However, today, as video conferencing is the main task for every endpoint supporting the standard, video codecs are required. H.323 uses video codecs from H.26X codec family for video encoding.
There is a list of technical requirements for audio codecs in H.323, since sound quality is essential in VoIP telephony. The requirements are as follows:
  Low level of delay;
  Lost packets recovering;
  High sound quality;
  Narrow bandwidth (no more than 8 kbit/s).

## Slide 79
G.7XX family codecs meet these requirements. However, bandwidth requirement is met by few G.7XX codecs.
By default, H.323 uses the G.711 codec with high bandwidth rate (about 64 kbit/s). However G.711 is considered to be outdated. Its sampling frequency (converting analog signal into digital signal) is only 8kHz, while G.722.1 has twice as high frequency (16kHz). Low frequency codecs such as G.723 (5.3/6.3kbps) and G.729 (8kbps) were used for the Internet connections initially. As for video codecs, every modern H.323 endpoint should support H.264, which become a standard.

## Slide 80: Quality of experience (QoE)
QoE is a measure of the delight or annoyance of a customer's experiences with a service (e.g., web browsing, phone call, TV broadcast).
QoE focuses on the entire service experience; it is a holistic concept, similar to the field of user experience, but with its roots in telecommunication.
QoE is an emerging multidisciplinary field based on social psychology, cognitive science, economics, and engineering science, focused on understanding overall human quality requirements.

## Slide 81: QoE measurement
As a measure of the end-to-end performance at the service level from the user's perspective, QoE is an important metric for the design of systems and engineering processes. This is particularly relevant for video services because – due to their high traffic demands –, bad network performance may highly affect the user's experience. So, when designing systems, the expected output, i.e. the expected QoE, is often taken into account – also as a system output metric and optimization goal.

## Slide 82
To measure this level of QoE, human ratings can be used. The mean opinion score (MOS) is a widely used measure for assessing the quality of media signals. It is a limited form of QoE measurement, relating to a specific media type, in a controlled environment and without explicitly taking into account user expectations. The MOS as an indicator of experienced quality has been used for audio and speech communication, as well as for the assessment of quality of Internet video, television and other multimedia signals, and web browsing. Due to inherent limitations in measuring QoE in a single scalar value, the usefulness of the MOS is often debated.

## Slide 83: Reference
Xingqin Lin, "An Overview of 5G Advanced Evolution in 3GPP Release 18," IEEE Communications Standards Magazine, Vol. 6, Iss. 3, pp. 77-83, Sep. 2022.
Wanshi Chen and Puneet Jain, 3GPP Release 18 Overview: A World of 5G-Advanced, Feb. 2, 2023. https://atis.org/?smd_process_download=1&download_id=1732913
Heinz MELLEIN, “5G ADVANCED & PROSPECT OF 3GPP R18 EVOLUTION AND BEYOND,” R&S Taiwan Webinar on 5G and beyond – June 2022. https://www.rohde-schwarz.taipei/data/activity/file/1656645404273831899.pdf
3GPP TS 23.501 V18.4.0 (2023-12) Technical Specification (Release 18)
Open5GS, https://open5gs.org/open5gs/docs/guide/01-quickstart/
Real-time Transport Protocol, Wikipedia, https://en.wikipedia.org/wiki/Real-time_Transport_Protocol
https://www.geeksforgeeks.org/real-time-transport-protocol-rtp/
https://trueconf.com/standart-h323.html
https://en.wikipedia.org/wiki/Quality_of_experience