## Slide 1: 理論教材A-1 次世代核心網路技術介紹
Lin-huang Chang
Department of Computer Science
National Taichung University of Education

## Slide 2: Outline
Introduction to Cellular/Mobile Networks
Overview of 5G/6G
  ITU-R IMT-2020 Requirements
  Features of 5G/6G
  3GPP Standardization
Introduction to 3GPP 5G/6G Specifications
  5G/6G Requirements and Key Performance Indicators
  The 5G System Architecture
  5G NR Radio Interface
  5G Radio Access Network (NG-RAN)
  5G Core Network

## Slide 3: Introduction to Cellular/Mobile Networks --Mobile Phone Generations (1)
1G (1979) | AMPS family | AMPS - N-AMPS, TACS - ETACS
 | Other | NMT, C-450, Hicap, Mobitex, DataTAC, CT1
2G (1991) | GSM/3GPP family | GSMCSD, HSCSD
 | 3GPP2 family | cdmaOne (IS-95)
 | AMPS family | D-AMPS (IS-54 and IS-136)
 | Other | CDPD, iDEN, PDC, PHS, CT2
2G transitional (2.5G, 2.75G, 2.9G) | GSM/3GPP family | GPRS, EDGE/EGPRS - Evolved EDGE
 | 3GPP2 family | CDMA2000 1X (TIA/EIA/IS-2000), CDMA2000 1X Advanced
 | Other | WiDEN, DECT
Source: https://en.wikipedia.org/wiki/Template:Cellular_network_standards

## Slide 4: Introduction to Cellular/Mobile Networks -- Mobile Phone Generations (2)
3G (1998) IMT-2000 (2001) | 3GPP family | UMTS (UTRA-FDD / W-CDMA (FOMA), UTRA-TDD LCR / TD-SCDMA, UTRA-TDD HCR / TD-CDMA)
 | 3GPP2 family | CDMA2000 1xEV-DO Release 0 (TIA/IS-856)
3G transitional (3.5G, 3.75G, 3.9G) | 3GPP family | HSPA (HSDPA, HSUPA), HSPA+ (DC-HSDPA), LTE (E-UTRA)
 | 3GPP2 family | CDMA2000 1xEV-DO Revision A (TIA/EIA/IS-856-A), EV-DO Revision B (TIA/EIA/IS-856-B), EV-DO Revision C
 | IEEE family | Mobile WiMAX (IEEE 802.16e), Flash-OFDM, iBurst (IEEE 802.20), WiBro
 | ETSI family | HiperMAN
Source: https://en.wikipedia.org/wiki/Template:Cellular_network_standards

## Slide 5: Introduction to Cellular/Mobile Networks -- Mobile Phone Generations (3)
4G (2009) IMT Advanced (2013) | 3GPP family | LTE Advanced (E-UTRA), LTE Advanced Pro (4.5G/4.9G)
 | IEEE family | WiMAX (IEEE 802.16m) (WiMax 2.1, WiBro)
5G (2018) IMT-2020 (2021) | 3GPP family | 5G NR, 5G-Advanced, NR-IIoT, LTE-M, NB-IoT
 | Other | DECT-5G
Source: Template:Cellular network standards - Wikipedia

## Slide 6: LTE Subscription Growth
Reference: Joe Barrett , Outlining the Roadmap to 5G , Journal of ICT
(Information and Communication Technology), Vol. 6 1&2, River Publishers, 2018

## Slide 7: LTE Network Investments and Launches

## Slide 8: LTE Deployment Facts (Reported by GSA)
LTE-Advanced 239 networks launched
LTE-Advanced Pro 123 networks launched or trailing
LTE-TDD 109 networks launched
Carrier Aggregation 290 networks launched or trialing
4x4 MIMO 114 networks launched or trialing
256QAM 96 operators have launched or using in DL
VoLTE 221 investing – 143 launched
eMBMS LTE Broadcast – 45 operators evaluating
– 3 have launched

## Slide 9: Using Three Core LTE-Advanced Features

## Slide 10: Percentage of mobile processors/platforms supporting specific UE categories
Source: GSA Chipset Report November 2018

## Slide 11: 5G/LTE/TD-LTE subscriptions by technology
  Source: Mobile subscriptions outlook– Ericsson Mobility Report

## Slide 12: 5G用戶成長評估
2024年第一季度，5G用戶增加了1.6億，總數超過17億
服務提供者繼續部署5G，到目前為止，約有300家營運商推出了商用網路
預計5G將在2028年超過4G成為佔主導地位
預計到到2029年底，5G用戶將達到56億
  Source: Mobile subscriptions forecast

## Slide 13: Announced 5G devices June 2023, by form factor
Source: GSA: 5G Device Ecosystem June 2023 Summary

## Slide 14: 投資5G SA的運營商數量
Source: 5G-Standalone September 2024 | GSA
Notes: Number of operators investing in 5G SA for public networks and number investing in any 3GPP 5G network
全球143家電信業者在61個國家/地區透過試驗、計劃或實際部署投資公共5G SA網路，這相當於23.1%的業者正在投資5G牌照、試驗或部署。
5G Device Ecosystem Summary Report - July 2024
https://www.linkedin.com/posts/global-5g-evolution_gsa-5g-device-ecosystem-july-2024-activity-7221844717544562688-3u_G
https://tele.net.in/expanding-ecosystem-new-gsa-report-shows-growth-in-commercial-5g-devices

## Slide 15: 支援5G SA設備的數量
Source: 5G-Standalone September 2024 | GSA

## Slide 16: 公布和已商用的5G SA設備（按形態分類）
Source: 5G-Standalone September 2024 | GSA

## Slide 17: Sub-6 GHz頻段的支援情況
6 GHz以下5G SA設備中最受支援的頻段模式在很大程度上與所有5G設備中最受支援的頻段模式相匹配，已知可滿足C頻段、2.6 GHz、2 GHz、1.8 GHz 和 700 MHz大多數設備。
Source: 5G-Standalone September 2024 | GSA

## Slide 18: Global mobile network data traffic (EB per month)
預計到2029年，5G在行動數據流量中的份額將增長到75%
預計到2029年，行動數據流量將以20%左右的複合年增長率增長
到2029年底，全球行動網路數據總流量將增長到每月約466 EB
資料來源：Ericsson Mobility Report June 2024
Source: Ericsson Mobility Report June 2024

## Slide 19: 台灣4G用戶平均上網使用量與去話分鐘變化
  【重上網、輕語音】的使用趨勢
    平均每月行動數據使用量：2018年7月達到17.2GB，較2017年7月(14.3GB)成長20.6%。
    平均每月去話分鐘數： 2018年7月降至41.6分鐘，較2017年7月衰退28%。
    2024年第1季：2,098.5萬4G用戶、873.5萬5G用戶、數據傳輸量2,999.3 Pbytes、去話分鐘數為1,736.4百萬分鐘數
Notes: =

## Slide 20: 2023 年全年及 2023 年上半年每張 SIM 卡 （不包括 M2M）的每月行動數據使用量
台灣(32.0)為全球第四，亞洲第一
  約南韓(17.3)的1.8倍
  約日本(9.8)的3.3倍
Source: Change at the top as growth slows
Notes: Mobile data usage per SIM (excl. M2M) per month
自2018年中以來，台灣的電信發展以網路流量吃到飽為主，但隨著台灣的運營商試圖讓市場回歸理性，使用量增長在過去幾年逐漸放緩。
相對較晚推出的5G（2020年中期）幫助台灣的運營商逆轉ARPU下降，因維兩家挑戰型行動網路運營商未能跟上進度。
網路流量吃到飽仍然是市場上的標準，但隨著5G推出，開始出現階梯式的價格結構。
https://tefficient.com/change-at-the-top-as-growth-slows
Mobile data usage per SIM (incl. M2M) per month, 2017
https://tefficient.com/unlimited-moves-the-needle-but-its-when-mobile-addresses-slow-fixed-internet-that-something-happens

## Slide 21: 持有手機民眾數位機會調查
手機族曾透過手機行動上網的比率由100年的35.3%大幅成長為107年的88.2%後，108年再增為89.8%。
  採用4G吃到飽方案連線的比率由106年的61.3%、107年的71.6%，再增為108年的79.2%
  55.9%同時申裝固網及手機行動上網服務的比率和107年相當
  31.2%僅仰賴手機上網，比107年成長3.2個百分點
每天手機上網時間逐年攀升
  女性滑手機雖然從107年的230分鐘降為211分鐘，但仍比男性略多8分鐘
  各年齡層中，以未滿20歲手機行動上網族的連網時間最長，由107年的282分鐘再增為312分鐘
Source: 國家發展委員會，108 年持有手機民眾數位機會調查報告，2022-08-31更新
100年 | 104年 | 105年 | 106年 | 107年 | 108年
92分鐘 | 179分鐘 | 201分鐘 | 204分鐘 | 211分鐘 | 206分鐘

## Slide 22: 手機功能應用情形

## Slide 23: 手機功能使用頻率

## Slide 24: 台灣民眾各設備的使用率
Source: Digital 2024 Taiwan

## Slide 25: 台灣民眾每日上網花費時間數據統計
Source: Digital 2024 Taiwan

## Slide 26: 台灣民眾網路應用服務的使用率
Source: 2023年台灣網路調查報告

## Slide 27: Introduction to Cellular/Mobile Networks -- Mobile Networks from GSM to 5G NR

## Slide 28: Introduction to Cellular/Mobile Networks -- Mobile Networks from GSM to 5G NR (Cont.)
GSM: developed to carry real time services, in a circuit switched manner
GPRS: the first step towards an IP based packet switched solution
  Using the same air interface and access method, TDMA (Time Division Multiple Access)
UMTS: 3G standard based on GSM
  Developing UTRAN and WCDMA
EPS (Evolved Packet System): purely IP based
  A flat, all-IP architecture with separation of control plane and user plane traffic
  Composed with E-UTRAN/LTE and packet-switched EPC (Evolved Packet Core)
5GS: Service-based Architecture and Network Slicing
  Architecture elements are defined as network functions
    Principles like modularity, reusability and self-containment of network functions
  Allows for controlled composition of a PLMN from the specified network functions with their specifics and provided services that are required for a specific usage scenario

## Slide 29: Outline
Introduction to Cellular/Mobile Networks
Overview of 5G
  ITU-R IMT-2020 Requirements
  Features of 5G
  3GPP Standardization
Introduction to 3GPP 5G Specifications
  5G Requirements and Key Performance Indicators
  The 5G System Architecture
  5G NR Radio Interface
  5G Radio Access Network (NG-RAN)
  5G Core Network

## Slide 30: What is 5G?
5th Generation
  ITU-R IMT-2020 Requirements
  3GPP Release 15~18 Specifications
Everything you need to know about 5G. (Qualcomm, Jan 2019)
https://www.qualcomm.com/5g/what-is-5g
What Is 5G? Cisco 5G news
https://www.cisco.com/c/en/us/solutions/what-is-5g.html
What is 5G?
https://aws.amazon.com/what-is/5g

## Slide 31: What is 5G?
5th Genaeration
What is 5G?
https://aws.amazon.com/what-is/5g

## Slide 32: International Telecommunication Union
A specialised agency of the United Nations that is responsible for issues that concern information and communication technologies
Comprises three sectors
  Radio communication (ITU-R)
    Established in 1927 as the International Radio Consultative Committee (CCIR)
      Became the ITU-R in 1992
    Manages the international radio-frequency spectrum and satellite orbit resources
    Develops standards for radiocommunication systems with the objective of ensuring the effective use of the spectrum
  Standardisation (ITU-T)
    Established in 1956 as the International Telephone and Telegraph Consultative Committee (CCITT)
      Became the ITU-T in 1993
    Standardizes global telecommunications (except for radio)
  Development (ITU-D)
    Established in 1992
    Helps spread equitable, sustainable and affordable access to information and communication technologies (ICT)
Source: International Telecommunication Union - Wikipedia

## Slide 33: International Mobile Telecommunications-2020 (ITU-R IMT-2020 Standard)
the requirements issued by the ITU-R of the ITU in 2015 for 5G networks, devices and services.
Capability | Description | 5G requirement | Usage scenario
Downlink peak data rate | Minimum maximum data rate technology must support | 20 Gbit/s | eMBB
Uplink peak data rate |  | 10 Gbit/s | eMBB
User experienced downlink data rate | Minimum data rate in dense urban test environment 95% of time (5th percentile) | 100 Mbit/s | eMBB
User experienced uplink data rate |  | 50 Mbit/s | eMBB
Latency | Radio network contribution to packet travel time | 4 ms | eMBB
 |  | 1 ms | URLLC
Mobility | Maximum speed for handoff and QoS requirements | 500 km/h | eMBB/URLLC
Connection density | Total number of devices per unit area | 106/km2 | mMTC
Energy efficiency | Data sent/received per unit energy consumption (by device or network) | Equal to 4G | eMBB
Area traffic capacity | Total traffic across coverage area | 10 Mbps/m2 | eMBB
Peak downlink spectrum efficiency | Throughput per unit wireless bandwidth and per network cell | 30 bit/s/Hz | eMBB
Source: IMT-2020 - Wikipedia

## Slide 34: Three Dimensions to Performance Improvements with Usage Scenarios for 2020 and Beyond
Source: ITU-R IMT 2020 Requirements (ITU-R M.2083, 2015)
eMBB
(enhanced Mobile
Broadband)
URLLC (Ultra-Reliable and Low
Latency Communications)
mMTC
(massive Machine
Type Communications)

## Slide 35: Enhancement of Key Capabilities from IMT-Advanced (4G) to IMT-2020 (5G)
Source: ITU-R M.2083-0 (Sep 2015)
大頻寬、低延遲、高可靠
High data rate
Low latency
High reliability
High density
High data rate
Low latency

## Slide 36: What is the Difference between 4G and 5G?
Everything you need to know about 5G.
Q: What are the differences between the previous generations of mobile networks and 5G?
A: The previous generations of mobile networks are 1G, 2G, 3G, and 4G.
First generation - 1G 1980s: 1G delivered analog voice.
Second generation - 2G Early 1990s: 2G introduced digital voice (e.g. CDMA- Code Division Multiple Access).
Third generation - 3G Early 2000s: 3G brought mobile data (e.g. CDMA2000).
Fourth generation - 4G LTE 2010s: 4G LTE ushered in the era of mobile broadband.
1G, 2G, 3G, and 4G all led to 5G, which is designed to provide more connectivity than was ever available before.
5G is a unified, more capable air interface. It has been designed with an extended capacity to enable next-generation user experiences, empower new deployment models and deliver new services.
With high speeds, superior reliability and negligible latency, 5G will expand the mobile ecosystem into new realms. 5G will impact every industry, making safer transportation, remote healthcare, precision agriculture, digitized logistics — and more — a reality.
Source: What is 5G? | Everything You Need to Know | 5G FAQ | Qualcomm

## Slide 37: Third Generation Partnership Project (3GPP)
3GPP is a consortium with seven national or regional telecommunication standards organizations as primary members ("organizational partners") and a variety of other organizations as associate members ("market representation partners"). The 3GPP organizes its work into three different streams: Radio Access Networks, Services and Systems Aspects, and Core Network and Terminals.
A global partnership created and managed by regional standards organizations
  Established in Dec 1998 with the goal of developing a specification for a 3G mobile phone system based on the 2G GSM system
Source: 3GPP - Wikipedia

## Slide 38: The Organizational Partners are:
Organizational Partners |  | 
Organization | Country/region | Website
Association of Radio Industries and Businesses (ARIB) | Japan | ARIB
Alliance for Telecommunications Industry Solutions (ATIS) | USA | ATIS
China Communications Standards Association (CCSA) | China | CCSA
European Telecommunications Standards Institute (ETSI) | Europe | ETSI
Telecommunications Standards Development Society (TSDSI) | India | TSDSI
Telecommunications Technology Association (TTA) | South Korea | TTA
Telecommunication Technology Committee (TTC) | Japan | TTC
Source: 3GPP - Wikipedia

## Slide 39: Standards: 3GPP standards are structured as Releases
Version[7] | Released[8] | Info
Release 15 | 2018 Q2 | First 5G NR ("New Radio") release. Support for 5G Vehicle-to-x service, IP Multimedia Core Network Subsystem (IMS), Future Railway Mobile Communication System[17]
Release 16 | 2020 Q3 | The 5G System – Phase 2: 5G enhancements, NR-based access to unlicensed spectrum (NR-U), Satellite access[18]
Release 17 | 2022 Q1 | TSG RAN: Several features that continue to be important for overall efficiency and performance of 5G NR: MIMO, Spectrum Sharing enhancements, UE Power Saving and Coverage Enhancements. RAN1 will also undertake the necessary study and specification work to enhance the physical layer to support frequency bands up to 71 GHz.TSG SA groups focused on further enhancements to the 5G system and enablers for new features and services: Enhanced support of: non-public networks, industrial Internet of Things, low complexity NR devices, edge computing in 5GC, access traffic steering, switch and splitting support, network automation for 5G, network slicing, advanced V2X service, multiple USIM support, proximity-based services in 5GS, 5G multicast broadcast services, Unmanned Aerial Systems (UAS), satellite access in 5G, 5GC location services, Multimedia Priority Service...[19]
Release 18 | 2023 Q4 | 5G-Advanced. Introducing further machine-learning based techniques at different levels of the wireless network. Edge computing, Evolution of IMS Multimedia Telephony Service, Smart Energy and Infrastructure, Vehicle-Mounted Relays, Low Power High Accuracy Positioning for industrial IoT scenarios, Enhanced Access to and Support of Network slicing, Satellite backhaul in 5G...[20][21][19]
Release 19 [22] | 2025 Q4 | 5G-Advanced.
Source: 3GPP - Wikipedia

## Slide 40: Core Network Evolution
Source: Introducing 3GPP
3G 4G 5G

## Slide 41: Radio Access Milestones
Source: Introducing 3GPP

## Slide 42: Generational Approach
Source: Introducing 3GPP

## Slide 43: 3GPP 5G Requirements
TR22.891 with 70s different user cases of four groups (SA1 finalized June 2016)

## Slide 44: Three Main 5G Cases and Examples
eMBB (enhanced Mobile Broadband)
mMTC (massive Machine Type Communications)
URLLC (Ultra-Reliable and Low Latency Communications)

## Slide 45: Features of 5G System Architecture
Service Based Architecture
  The architecture elements are defined as network functions
  Adopts principles like modularity, reusability and self-containment of network functions
Common Core Network
  Enables to operate with different access networks
Network Slicing
  Allows for controlled composition of a PLMN from the specified network functions with their specifics and provided services that are required for a specific usage scenario
Application Support
  A new QoS model enables differentiated data services to support diverse application requirements
Source: System architecture milestone of 5G Phase 1 is achieved

## Slide 46: R15 and R16 NR Milestones
[Dec 2017]
Non-standalone
(NSA) 5G NR
mode for eMBB
(Option 3)
[June 2018] Standalone (SA) 5G NR (Option 2) approved
by TSG #80 Plenary Meeting
5G Non-Standalone (NSA): The existing LTE radio access and core network (EPC)
is used as an anchor for mobility management and coverage to add the 5G carrier
5G Standalone (SA): A new 5G Packet Core comprising of 5G New Radio (5G NR)
and 5G Core Network (5GC) is introduced with several new capabilities built inherently

## Slide 47: 3GPP Ongoing Releases
Stage 1: an overall service description from the user’s standpoint
Stage 2: an overall description of the organization of the network functions
to map service requirements into network capabilities
Stage 3: the definition of switching and signalling capabilities needed to support services defined in stage 1
ASN.1: Standard interface description for defining data structures
Source: Specifications & Technologies: 3GPP

## Slide 48: 3GPP ASN.1
ASN.1 (Abstract syntax notation)
  A standard interface description language
  for defining data structures that can be serialized
  and deserialized in a cross-platform way (Wiki)
Object identifiers maintained by ETSI EG 200 351
  ccitt|itu-t / identified-organization / etsi / mobileDomain
    / eps-Access
    / ngran-access

## Slide 49: 3GPP Release Timetable

## Slide 50: 3GPP Release Timetable (R18)
Source: Release 18

## Slide 51: R18 overview

## Slide 52: 3GPP Release Timetable (R19)
Source: 3GPP Release

## Slide 53: Rel-19 content was decided at the December 2023 TSGs (#102):
Source: Release 19

## Slide 54: Rel-19 Content definition Process and timeline
Source: Rel-18 Status and Rel-19 Progress in TSG SA

## Slide 55: Rel-19 Topics
Source: Rel-18 Status and Rel-19 Progress in TSG SA

## Slide 56: Release 18 and Release 19 timelines.
Source: The 3GPP's System of Parallel Releases

## Slide 57: Rel-20 content to be decided in the 1H 2025.
Source: Release 20

## Slide 58: 6G願景

## Slide 59: 6G關鍵技術

## Slide 60: 6G標準推動時程

## Slide 61: TSG RAN – Radio Access Network
The 3GPP TSG Radio Access Network (RAN) is responsible for the technical co-ordination of the specification work done in the following Working Groups:
  RAN1 – Radio Layer 1 (Physical layer)
  RAN2 – Radio layer 2 and Radio layer 3 Radio Resource Control
  RAN3 – UTRAN/E-UTRAN/NG-RAN architecture and related network interfaces
  RAN4 – Radio Performance and Protocol Aspects
  RAN5 – Mobile terminal conformance testing
RAN is responsible for the GERAN, UTRAN, E-UTRAN, NG-RAN and beyond, including their internal structures and functions, of systems for evolved GERAN, UTRAN, E-UTRAN, NG-RAN and beyond.
Source: TSG Radio Access Network (RAN); 3GPP

## Slide 62: 5G/NR MmWave Bands
5G/NR - mmWave |  |  | 
Band | Frequencies [GHz] | BW [MHz] | Duplex mode
n257 | 26.5-29.5 | 50-400 | TDD
n258 | 24.25-27.5 | 50-400 | TDD
n260 | 37.0-40.0 | 50-400 | TDD
TBD | 37.0-43.5 | 50-400 | TDD

## Slide 63: 5G/NR Spectrum Below 6 GHz
Band | Frequencies [GHz] | BW [MHz] | Duplex mode
n77 | 3300-4200 | 10-100 | TOD
n78 | 3300-3800 | 10-100 | TOD
n79 | 4400-5000 | 40-100 | TOD
n80 | 1710-1785/N/A | 5-30 | SUL
n81 | 880-915/N/A | 5-20 | SUL
n82 | 832-862/N/A | 5-20 | SUL
n83 | 703-748/N/A | 5-20 | SUL
n84 | 1920-1980/N/A | 5-2. | SUL

## Slide 64: 5G/NR Re-farmed Spectrum
Band | Identifier | Frequencies [GHz] | BW [MHz]
n1 | IMF Core Band | 1920-1980/2110-2170 | 5-20
n2 | PCS 1900 | 1850-1910/1930-1990 | 5-20
n3 | 1800 | 1710-1785/1805-1880 | 5-30
n5 | 850 | 824-849/869-894 | 5-20
n7 | IMF Extension | 2500-2570/2620-2690 | 5-20
n8 | 900 | 880-915/925-960 | 5-20
n13 | US 700 Upper C | 777-787/746-756 | tbd
n20 | CEPT800 | 832-862/791-821 | 5-20
n25 | PCS1900G | 1850-1915/1930-1995 | tbd
n26 | E850 Upper | 814-849/859-894 | tbd
n28 | APT 700 | 703-748/758-8035-20 | 5-20
n34 | TDD 2000 Upper | 2010-2025 | tbd
n38 | IMF Extension Gap | 2570-2620 | 5-20
n39 | China TDD 1900 | 1880-1920 | tbd
n40 | TDD 2300 | 2300-2400 | tbd
n41 | TDD 2600 | 2496-2690 | 10-100
n50 | TDDL-band | 1432-1517 | 5-80
n51 | TDDL-band, local | 1427-1432 | 5
n66 | AWS Extension | 1710-1780/2110-2200 | 5-40
n70 | AWS-3/4 | 1695-1710/1995-2020 | 5-25
n71 | US 600 | 663-698/617-652 | 5-20
n74 | FDDL-band | 1427-1470/1475-1517 | 5-20
n75 | Extended SDL L-band | N/A/1432-1517 | 5-20
n76 | Extended SDL L-band, local | N/A/1427-1432 | 5

## Slide 65: International 5G scoreboard Overview of 5G developments
Below you will find tables and charts about 5G rollout and 5G spectrum awards in major international markets.
Source: 5G Scoreboard – 5G Observatory

## Slide 66: Chart: Authorised 5G spectrum in international markets
Reporting period: May 2024
Source: Sourced from the PolicyTracker Spectrum Database
& FCC 2022 Communications Marketplace Report.
Notes: 請注意：對於歐盟，數據代表歐盟 27 國統一的頻譜。一些國家可能為 5G 分配了更多頻譜，而另一些國家可能分配了更少或沒有頻譜。

## Slide 67: Table: Main bands authorised for 5G in international markets
Reporting period: May 2024
Source: Sourced from the PolicyTracker Spectrum Database
& FCC 2022 Communications Marketplace Report.

## Slide 68: 5G System Architecture (Non-Roaming Service-Based)

## Slide 69: 5G Architecture Options (TR38.801)

## Slide 70: 4G/5G Control Plane Protocol Stack
4G (Option 1)
5G (Option 2)

## Slide 71: 4G/5G User Plane Protocol Stack for 3GPP Access
4G (Option 1)

## Slide 72: 5G NSA (Release 15)
Three models of NSA Option 3 – Traffic split at eNB
  Option 3a – Traffic split at S-GW
  Option 3x – Traffic split at gNB

## Slide 73: Release 16
Feature or Study Item: Study on Communication for Automation in Vertical Domains | FS_CAV
Building Block: Stage 1 of MONASTERY2 | MONASTERY2
Building Block: Study on MONASTERY2 | FS_FRMCS2
Building Block: Study on positioning use cases | FS_5G_HYPOS
Building Block: Study on LAN Support in 5G | FS_5GLAN
Building Block: Study on Maritime Communication Services over 3GPP system | FS_MARCOM
Building Block: Study on enhancements of Public Warning System | FS_ePWS
Building Block: Study on eLSTR | FS_eLESTR
Building Block: Study on a Layer for User Centric Identifiers and Authentication | FS_LUCIA
Feature or Study Item: Study on using Satellite Access in 5G | FS_5GSAT
Feature or Study Item: Study on enhancements to IMS for new real time communication services | FS_enIMS
Building Block: Study on 5G message service for MIoT | FS_5GMSG
Building Block: Study on Business Role Models for Network Slicing | FS_BMNS
Building Block: Stage 1 of PARLOS | PARLOS
Feature or Study Item: 5G Voice Service Continuity | 5GVSC
Feature or Study Item: New Services and Markets Technology Enablers – Phase 2 | SMARTER_Ph2
Feature or Study Item: Study on Improvement of V2X Service Handling | FS_V2XIMP
Feature or Study Item: Enhancements to IMS for new real time communication services | enIMS
Feature or Study Item: QoS Monitoring | QoS_MON
Feature or Study Item: Study on Remote Identification of Uncrewed Aerial Systems | FS_ID_UAS
Feature or Study Item: Study on Extended Provision of Connectivity Opportunities | FS_EPCO
Building Block: Stage 1 of 5G_HYPOS | 5G_HYPOS
Building Block: Stage 1 of User Identities and Authentication | UIA
Building Block: Stage 1 of MARCOM | MARCOM
Building Block: Stage 1 of ePWS | ePWS
Building Block: Stage 1 of eLSTR | eLSTR
Building Block: Stage 1 of Multi-device and multi-identity | MuD
Feature or Study Item: Inter-RAT Mobility requirements for real time service | MOBRT
Feature or Study Item: LAN support in 5G | 5GLAN
Feature or Study Item: Service requirements for cyber-physical control applications in vertical domains | cyberCAV
Feature or Study Item: Enhancement of LTE for Efficient delivery of Streaming Service | eLSTR
Feature or Study Item: Policy delivery to UE for background data transfer | PDBDT
Feature or Study Item: Integration of Satellite Access in 5G | 5GSAT
Feature or Study Item: Maritime Communication Services over 3GPP System | MARCOM
Feature or Study Item: User Identities and Authentication | UIA
Feature or Study Item: 5G positioning services | 5G_HYPOS
Building Block: Stage 1 of 5GLAN | 5GLAN
Feature or Study Item: 5G message service | 5GMSG
Feature or Study Item: Business Role Models for Network Slicing | BRMNS
Feature or Study Item: Improvement of V2X service Handling | V2XIMP
Building Block: Message Service Within the 5G System requirements | MSGin5G
Building Block: Business Role Models for Network Slicing | BRMNS
Source: 3GPP work items for: S1

## Slide 74: Release 17
Building Block: Stage 1 of MINT | MINT
Building Block: Stage 1 of ATRAC | ATRAC
Feature or Study Item: Enhanced Calling Name Service Analytics Interworking | eCNAM_An
Building Block: Stage 1 of eCPSOR_CON | eCPSOR_CON
Feature or Study Item: Broadcast / Multicast requirements supporting Mission Critical Services in 5G | 5MBS_eMC
Building Block: Stage 1 of MuDE | MuDE
Building Block: Stage 1 of NCIS | NCIS
Building Block: Stage 1 of AVPROD | AVPROD
Building Block: Stage 1 of MPS2 | MPS2
Building Block: Stage 1 of CMED | CMED
Building Block: Stage 1 of REFEC | REFEC
Building Block: Stage 1 of EAV | EAV
Building Block: Stage 1 of MUSIM | MUSIM
Building Block: Stage 1 of eCAV | eCAV
Feature or Study Item: Complete Gap Analysis for Railways Mobile Communication System | MONASTERYEND
Feature or Study Item: Study on Future Railway Mobile Communication System3 | FS_FRMCS3
Feature or Study Item: IMS emergency support for Stand-alone Non-Public Network (SNPN) | IESNPN
Feature or Study Item: Verification-modified Calling Name Display | VMOD_DISPLAY
Building Block: Study on MINT | FS_MINT
Building Block: Study on MUSIM | FS_MUSIM
Building Block: Study on eCAV | FS_eCAV
Building Block: Stage 1 of Remote Identification of Uncrewed Aerial Systems | ID_UAS
Building Block: Study on CMED | FS_CMED
Building Block: Study on ATRAC | FS_5G_ATRAC
Building Block: Study on REFEC | FS_REFEC
Building Block: Study on EAV | FS_EAV
Building Block: Stage 1 of 5GSAT | 5GSAT
Feature or Study Item: NPN support of PWS | NPN_PWS
Building Block: Study on AVPROD | FS_AVPROD
Building Block: Study on NCIS | FS_NCIS
Building Block: Study on MPS2 | FS_MPS2
Source: 3GPP work items for: S1

## Slide 75: Release 18
Building Block: Study on VMR | FS_VMR
Building Block: Study on PALS | FS_PALS
Feature or Study Item: Subscriber-aware Northbound API access | SNA
Feature or Study Item: Study on FRMCS Phase 4 | FS_FRMCS_Ph4
Building Block: Study on TACMM | FS_TACMM
Feature or Study Item: Support for Service Function Chaining | SFChain
Building Block: Stage 1 for EASNS | EASNS
Building Block: Stage 1 for 5TRS | 5TRS
Building Block: Stage 1 for Ranging | Ranging
Feature or Study Item: Data Integrity in 5GS | DI_5G
Feature or Study Item: Low Power High Accuracy Positioning for industrial IoT scenarios | LPHAP
Building Block: Stage 1 of Evolution of IMS Multimedia Telephony Service | eMMTEL
Building Block: Stage 1 of AMMT | AIML_MT
Building Block: Stage 1 of PALS | PALS
Building Block: Stage 1 of Smart Energy and Infrastructure | SEI
Feature or Study Item: Signal level Enhanced Network Selection | SENSE
Feature or Study Item: 5G system with satellite access to Support Control and/or Video Surveillance | SCVS
Building Block: Stage 1 of 5GSATB | 5GSATB
Building Block: Stage 1 of TACMM | TACMM
Building Block: Stage 1 of VMR | VMR
Building Block: Stage 1 of PIRates | PIRates
Feature or Study Item: Service exposure interfaces for industry | EXPOSE
Building Block: Stage 1 of MPS_WLAN | MPS_WLAN
Feature or Study Item: Ad hoc Group Communication support in Mission Critical Services | AHGC
Feature or Study Item: Sharing administrative configuration between interconnected MCX Service systems | SACI_MCS
Building Block: Study on traffic characteristics and performance requirements for AI/ML model transfer in 5GS | FS_AIML_MT
Feature or Study Item: Guidelines for Extra-territorial 5G Systems | FS_5GET
Building Block: Study on EASNS | FS_EASNS
Feature or Study Item: Study on Off-Network for Rail | FS_OffNetRail
Building Block: Study on 5TRS | FS_5TRS
Building Block: Study on 5G Smart Energy and Infrastructure | FS_5GSEI
Building Block: Study on Ranging | FS_Ranging
Building Block: Study on Enhancements for Residential 5G | FS_Resident
Building Block: Study on Personal IoT Networks | FS_PIN
Building Block: Study on evolution of IMS multimedia telephony service | FS_MMTELin5G
Feature or Study Item: Study on sharing administrative configuration between interconnected MCX Service systems | FS_SACI_MCS
Feature or Study Item: Modified PRINS for roaming service providers in 5G | Roaming5G
Building Block: Stage 1 of Roaming5G | Roaming5G
Feature or Study Item: SMS over IMS to emergency centre | SMS2EC
Source: 3GPP work items for: S1

## Slide 76: Release 19
Feature or Study Item: Measurement Data Collection | MeasureData
Feature or Study Item: PS Data Off for IMS Data Channel Service | IMSDCDataOff
Feature or Study Item: Edge Computing for Industrial Scenarios | EDGINDUS
Building Block: Roaming Value-Added Services | RVAS
Feature or Study Item: Supporting UE Mobility for XR Services | XRMobility
Feature or Study Item: Study on Interconnect of SNPN | FS_ISN
Building Block: Study on roaming value added services | FS_RVAS
Building Block: Study on satellite access - Phase 3 | FS_5GSAT_Ph3
Building Block: Study on (Stage 1 of) UAV Phase 3 | FS_UAV_Ph3
Feature or Study Item: Study on Upper layer traffic steering, switching and split over dual 3GPP access | FS_DualSteer
Building Block: Study on Energy Efficiency as service criteria | FS_EnergyServ
Feature or Study Item: Study on Network of Service Robots with Ambient Intelligence | FS_SOBOT
Building Block: Stage 2 of Minimization of Service Interruption During Core Network Failure Phase 2 | MINT_Ph2
Building Block: (stage 1 of) MPS for Messaging services | MPS4msg
Feature or Study Item: Interworking of Non-3GPP Digital Terrestrial Broadcast Networks with 5GS Multicast Broadcast Services | DTT4MBS
Feature or Study Item: Multi-path relay | MultiRelay
Building Block: Stage 1 of Satellite access Phase 3 | 5GSAT_Ph3
Feature or Study Item: UE-to-UE multi-hop relay | UEMHopRelay
Building Block: Stage 1 of Integrated Sensing and Communication | Sensing
Feature or Study Item: Non-Public Network (NPN) security considerations | SecNPN
Building Block: Stage 1 of Localized Mobile Metaverse Services | Metaverse
Building Block: (Stage 1 of) Indirect Network Sharing | NetShare
Feature or Study Item: AI/ML Model Transfer Phase 2 | AIML_MT_Ph2
Feature or Study Item: FRMCS Phase 5 | FRMCS_Ph5
Building Block: Stage 1 of Uncrewed Aerial System Phase 3 | UAS_Ph3
Building Block: Stage 1 of Energy Efficiency as Service Criteria | EnergyServ
Feature or Study Item: Edge Computing Considering the Operational Needs of Service Hosting Environment | EdgeOpNeeds
Feature or Study Item: Upper layer traffic steering, switching and splitting over dual 3GPP access | DualSteer
Feature or Study Item: Ambient power-enabled Internet of Things | AmbientIoT
Feature or Study Item: Local traffic routing for multi-access UE | LTR_MA
Building Block: Stage 1 of Ambient power-enabled Internet of Things | AmbientIoT
Feature or Study Item: Upper layer traffic steering and switching over dual 3GPP access | DualSteer
Feature or Study Item: Timestamp Information Exposure for critical IoT Applications | TIE_IoTAPP
Building Block: Stage 1 for MonSta | MonSTra
Feature or Study Item: Minimization of Service Interruption During Core Network Failure Phase 2 | MINT_Ph2
Feature or Study Item: Monitoring of signalling traffic in 5G | MonSTra
Feature or Study Item: Proximity-based Services in 5GS Phase 3 | 5G_ProSe_Ph3
Feature or Study Item: Interconnect of SNPN | ISN
Feature or Study Item: Study on Supporting of Railway Smart Station Services | FS_RAILSS
Building Block: Study on Integrated Sensing and Communication | FS_Sensing
Building Block: Study on Ambient power-enabled Internet of Things | FS_AmbientIoT
Building Block: Study on Localized Mobile Metaverse Services | FS_Metaverse
Building Block: Study on Network Sharing Aspects | FS_NetShare
Feature or Study Item: Study on FRMCS Phase 5 | FS_FRMCS_Ph5
Feature or Study Item: Study on AI/ML Model Transfer Phase2 | FS_AIML_MT_Ph2
Source: 3GPP work items for: S1

## Slide 77: Release 20
Feature or Study Item: Study on satellite access - Phase 4 | FS_5GSAT_Ph4
Feature or Study Item: Study on FRMCS Phase 6 | FS_FRMCS_Ph6
Feature or Study Item: Study on Energy Efficiency as Service Criteria Phase 2 | FS_EnergyServ_Ph2
Feature or Study Item: Indirect Network Sharing on Satellite Access Network | INS_SAT
Feature or Study Item: Indirect Network Sharing Phase 2 | NetShare_Ph2
Feature or Study Item: Resident Phase 2 | Resident_Ph2
Feature or Study Item: Combined QoS configuration and monitoring | CombQoS
Feature or Study Item: Legacy Residential Gateway Supporting 5G LAN-type Service | LegacyRG_5GLAN
Feature or Study Item: Study on 6G Use Cases and Service Requirements | FS_6G-REQ
Feature or Study Item: Exposure for Virtual Network information and capability | VNExposure
page generated from database: 2024-11-12 10:16:04
Source: 3GPP work items for: S1

## Slide 78: Release 18
These improvements consist both in enhancements of concepts/Features introduced in the previous Releases and in the introduction of new topics.
Some of the key improvements are:
  a further integration of the Satellite (NTN) access (introduced in Rel-17) in the 5G System (5GS),
  a more efficient support of Internet of Things (IoT), Machine-Type Communication (MTC), including by satellite coverage
  and also several aspects of proximity communication and location (Sidelink, Proximity, Location and Positioning, better support of the industrial needs (Verticals, Industries, Factories, Northbound API), Multicast and Broadcast Services (MBS), Network Slicing or Uncrewed Aerial Vehicles (UAV).
As for the new topics, some of the key aspects are:
  Energy Efficiency (EE)
  Artificial Intelligence (AI)/Machine Learning (ML)
  eXtended, Augmented and Virtual Reality (XR, AR, VR), immersive communications
Source: The 3G4G Blog: 3GPP Release 18 Description and Summary of Work Items

## Slide 79: Non-Terrestrial Networks (NTN) (1/2)
Non-terrestrial networks (NTN) are networks or segments of networks that use either Uncrewed Aircraft Systems (UAS) operating typically between 8 and 50km altitudes, including High Altitude Platforms (HAPs) or satellites in different constellations to carry a transmission equipment relay node or a base station:
  LEO (Low Earth Orbit): Circular orbit in altitudes of typ. 500-2.000km (lower delay and better link budget but larger number of satellites needed for coverage)
  MEO (Medium Earth Orbit): Circular orbit in altitudes of typ. 8.000-20.000km
  GEO (Geostationary Earth Orbit): Circular orbit 35.786 km above the Earth's equator (Note: Due to gravitational forces a GEO satellite is still moving within a range of a few km around its nominal orbital position).
  HEO (Highly Elliptical Orbiting): Elliptical orbit around the earth.
By Joern Krause, 3GPP MCC. Source: Non-Terrestrial Networks (NTN)

## Slide 80: Non-Terrestrial Networks (NTN) (2/2)
Figure : Illustration of the classes of orbits of satellites [source: TR 22.822]
By Joern Krause, 3GPP MCC. Source: Non-Terrestrial Networks (NTN)

## Slide 81: Two types of modes or "payload" can be distinguished
  Non-regenerative payload (also called "bentpipe payload" (considering the path from the gateway via spaceborne/airborne platform to the UE) or "transparent mode"): A spaceborne/airborne platform with no on-board processing capabilities that changes the frequency carrier of the received uplink RF signal, filters and amplifies it before transmitting it on the downlink, i.e. the platform corresponds to an analogue RF repeater;
  Regenerative payload (or non-transparent mode): a spaceborne/airborne platform that has on top of RF filtering, frequency conversion and amplification also on-board processing capabilities (for demodulation/decoding, switching and/or routing, coding/modulation) so this spaceborne/airborne platform has base station functions on board.
Figure : Transparent vs. Regenerative payload
and elliptic beam patterns [source: 38.811]
By Joern Krause, 3GPP MCC
Source: Non-Terrestrial Networks (NTN)

## Slide 82: Figure : Illustration of elevation angle and propagation delay [source: TR 38.811]
By Joern Krause, 3GPP MCC. Source: Non-Terrestrial Networks (NTN)

## Slide 83: Non-terrestrial networks (NTN) have a number of characteristics that require adaptations in comparison to terrestrial networks (TN) (source: TR 38.811) including:
  Motion of the space/aerial vehicles: Only for GEO the satellite stays rather stable over the earth like in terrestrial networks. For LEO and MEO the satellites are moving with high velocity which leads to moving cell patterns, higher Doppler shifts/variations, faster propagation delay variations - requiring enhanced beam management (based on information about the predictable movement of the satellite (ephemeris) and the location/movement of the UE, the satellite network could know which beam and satellite covers the UE best).
By Joern Krause, 3GPP MCC. Source: Non-Terrestrial Networks (NTN)

## Slide 84: Satellite / Non-Terrestrial Network (NTN) User plane: “5G system with satellite backhaul”
The work item "5G system with satellite backhaul" (5GSATB) specifies two different aspects: the 5G system enhancements needed to support dynamic satellite backhaul; and the User Plane Function (UPF) onboard GEO satellite.
Figure: satellite backhaul (satellite link used between 5GC and 5GRAN)

## Slide 85: ITU-R WP 5D agrees on “IMT-2030 Framework” (June 2023)​
At its June 2023 meeting, ITU-R WP 5D has agreed the draft new Recommendation “Framework and overall objectives of the future development ​of IMT for 2030 and beyond”*​​, which can be considered as the basis for the standardisation fora to develop the next generation of​ IMT standards​​.
​This draft Recommendation addresses:
  ​​Trends of IMT-2030
  Usage scenarios of IMT-2030
  Capabilities of IMT-2030
  Considerations of ongoing development
Source: IMT towards 2030 and beyond (IMT-2030)

## Slide 89: ITU-R Report on “Future Technology Trends” (December 2022)
ITU-R WP 5D developed a new ITU-R Report on “Future Technology Trends”, which has been published as Report ​ITU-R M.2516​ in December 2022. This Report provides a broad view of future technical aspects of terrestrial IMT systems considering the timeframe up to 2030 and beyond, characterized with respect to key emerging services, applications trends and relevant driving factors and is applicable to radio interfaces, mobile terminals, and radio access networks by considering the timeframe up to 2030 and beyond.
Source: IMT towards 2030 and beyond (IMT-2030)

## Slide 90: ITU-R Working Party 5D agrees on the overview timeline for IMT towards the year 2030 and beyond (June 2022)
The work and discussion on a new timeline started in WP 5D #37 and during its meeting #41 (June 2022), ITU-R WP 5D agreed on the overview timeline for IMT towards the year 2030 and beyond.
The agreement is described in detail in Attachment 2.12 to Chapter 2 of Document 5D/1361 (Meeting report WP 5D #41) and describes the process and shows the anticipated deliverables for the development of IMT towards 2030 and beyond. It has been agreed that the well-known process and deliverable formats utilized for IMT-2000, IMT-Advanced, and IMT-2020 should be utilized also for IMT towards 2030 and beyond and considered as a “model” for the IMT deliverables to leverage on the prior work.​
Source: IMT towards 2030 and beyond (IMT-2030)

## Slide 92: Workshop on “IMT for 2030 and beyond” (14th June 2022)
ITU-R WP 5D held a full-day Workshop on “IMT for 2030 and beyond”, with total 348 participants in an integrated physical and remote participants arrangement. The objective of the Workshop was to provide WP 5D delegates with an overview of ongoing worldwide research activities, initiatives, and views related to future mobile communications targeting 2030 and beyond (details see here).
Fourteen presentations were made from various ITU-R members, external organizations, research projects and academia and in reflecting on the presentations, the following graphic considers keyword theme from each presentation organized within the context of the currently planned sections of the WP 5D working document towards a preliminary draft new Recommendation ITU-R M.[IMT.VISION 2030 AND Beyond]:
Source: IMT towards 2030 and beyond (IMT-2030)

## Slide 93: ​FIGURE : Keywords in the presentations and mapping with [IMT.vision 2030 AND Beyond] sections ​
Source: IMT towards 2030 and beyond (IMT-2030)